## Slide 1: TAS Data Explanation
Anique Altena
11-03-2024

## Slide 2: Data
Config.txt
  Microphone locations compared to the centre of the array
Microphone measurements
  Pressure fluctuations measured by the 64 microphones over time (fs = 50000Hz)
GPS
  Latitude, Longitude and Altitude measurements for each drone
  Time vectors are included in some form (note that fs changes per drone and is not consistent for some drones)
Info.txt
  Array location, broken microphones
  Start times of microphone measurements, start times of the segments I selected for you, start time of the GPS
11-03-2024

## Slide 3: Your Approach
Calculate the time at which the segment I selected for you starts and ends:
  Start segment = start time microphone array + start time selected segment
  End segment = start segment + 5 seconds
Find the start and end time of the segment in the corresponding GPS file
11-03-2024

## Slide 4: Warning!
Once you have performed beamforming and validated the result with the GPS track, you will find that they are off:
This Δt comes from the fact that the internal clock of the microphone array is not exactly aligned with the one in the GPS. There is a bias. (Think about your own watch, it is always a bit ahead or behind, never exactly correct)
You are allowed to shift the GPS data such that it fits the array data. In fact, I would be extremely happy if you could tell me how many seconds this shift is .
11-03-2024
Time
GPS
Array
Δt